## Slide 1: Status of the EIC R&D
Kondo Gnanvo
EIC Weekly Meeting, Nov. 21, 2016

## Slide 2: Status of the new U-V readout strips: 10 cm x10 cm prototype
U-V strip 2D readout board
The readout strip pitch = 400 μm ⇨ improve overall spatial resolution, reduce noise and strip occupancy
Larger U-V stereo-angle of 30.1o provide significant improvement of the spatial resolution in the radial direction
The small prototype is almost assembled => waiting for the new Gas box from CERN
The Zebra connection is the next step

## Slide 3: EIC U-V readout strips: Zebra connection parts
Electrical contacts between the strips and the FE electronics done with zebra connectors on the outer radius side
no connectors and metallized holes (vias) on the readout board ⇨Lower production cost and risks
Contact of the U and V strips are done on either side of the R/O foil
Zebra holder on the adapter

## Slide 4: Status of the Chromium GEM (Cr-GEM)
old batch: Proto I
New batch: Proto II
For the new batch of Cr-GEMs, Cr layer foils seems even thinner than our first foils
Foils almosr transparent to the Cr, probably less than 100 nm
Inquiry with Rui @ CERN to try to understand

## Slide 5: Status of the Chromium GEM (Cr-GEM)
3 new Cr-GEM foils and 1 hybrid Cr-GEM
Hybrid Cr-GEM has the Cu completely removed on only on side
    top side is Cr electrode and bottom side Cu electrode
Study hybrid triple Cr-GEM with hybrid GEM used for the third GEM (on top of the anode readout)
    Can we address dead area issue at the high rate ?
Hybrid Cr-GEM
Copper electrode
Chromium electrode

## Slide 6: Ideas for a 2D zigzag strip readout

## Slide 7: Radial TPC (RTPC) for TDIS in Hall A

## Slide 8: Chevron / zigzag readout strips for TDIS rTPC
1 mm
20 mm
0.5 mm
90o
28.3 mm
V-strips
U-strips
1 mm cluster charges